## Slide 1: Basic Hydrology & Hydraulics: DES 601
Module XXX
TITLE

## Slide 2: Module Outline
Background
Applicability
Using the Tool
Module 1

## Slide 3: Acronyms
HDM: TxDOT Hydraulic Design Manual 2015 Ed. (on-line)
HDS2: FHWA-NHI-02-001 Highway Hydrology
ROT: Rule-of-Thumb
Module 1

## Slide 4: Background
Culverts, bridges, and other obstructions change the water surface profile in a channel
The addition or removal of flow from a stream may affect the water surface downstream and possibly upstream
The effect on the water surface near the structure is known by modeling the receiving stream
Module 1

## Slide 5: Background
Boundary effects can propagate into region of interest
Limited guidance on where to locate boundaries in HDM standard-step backwater method
Want boundary effects small in region of interest
Region of interest

## Slide 6: Background
The designer would like to avoid modeling an entire stream system (many structures) to study the change at single location (one structure)
TxDOT Research 0-6841 examined existing literature and conducted a HEC-RAS study to develop Rules-Of-Thumb (ROT) for selecting boundary location distances
Module 1

## Slide 7: Background
How far do boundary effects extend?

## Slide 8: Background
How far do boundary effects extend?
Treat As Single Bridge
ROT Boundaries overlap Consider upstream bridge
Boundary here
Structure of Interest

## Slide 9: Applicability
ROT are intended for examining a single location
Also identifies if additional locations should be included
  Locate boundary distances for structure of interest
  If nearby structures boundaries have overlap, then include these in overall modeling effort

## Slide 10: Rules-Of-Thumb
Four rules emerged from the study:
Boundary distance is approximately where the estimate is the result of Equation 4 Modeling a Change in Flowrate through Detention or Additional Pavement on the Receiving Stream, FHWA/TX-15/0-6841-1

## Slide 11: Rules-Of-Thumb
Four rules emerged from the study:
Boundary distance is approximately 20 to 30 bank full channel widths Wildland Hydrology, 2013. References in support of stream restoration, erosion control, and geomorphology. Accessed on July 7, 2013 at http://www.wildlandhydrology.com/html/references_.html

## Slide 12: Rules-Of-Thumb
Boundary distance approximately 100 to 500 feet approaching (upstream) and 300 to 1,500 feet departing (downstream) Nebraska Department of Roads. (2015). Hydraulic Analysis Guidelines. Bridge Division.

## Slide 13: Rules-Of-Thumb
Boundary distance L approximately where D is bank full depth and S0 is the channel slope. Samuels, P. (1989). Backwater Lengths in Rivers. Proceedings of the Institution of Civil Engineers (p. 571582). Great Britian: Hydraulics Research. Castellarin, A., Baldassarre, G. D., Bates, P., and Brath, A. (2009). Optimal Cross-Sectional Spacing in Preissmann Scheme 1D Hydrodynamic Models. Journal of Hydraulic Engineering , 96-105.

## Slide 14: Rules-Of-Thumb
The four rules produce different results, but most are of similar magnitude
Ultimate decision is designer’s judgment
To facilitate the calculations involved a spreadsheet-based tool was built that implements the four rules, then the designer chooses a preferred rule and can use that value to establish modeling boundaries

## Slide 15: Using the Tool
BoundaryDistanceRuleOfThumb-2015.xlsm
Implements the various ROT distances; the designer must make the decision which guidance to follow, although the tool reports several different guidelines

## Slide 16: Using the Tool – Needed Values
Reference Discharge – The original pre-change discharge at the location
Test Discharge – The added or reduced discharge at the location
Structure opening flow area
Far field flow area
Far field top width
Bank full flow depth
Bank full flow width
Curved or Straight Channel
Skewed or Aligned Hydraulic Structure

## Slide 17: Structure Opening Flow Area
Elevation view looking downstream
Flow area of the structure at Soffit flow depth

## Slide 18: Far-field flow area
Elevation view looking downstream
Flow area of the channel away from the structure at the Soffit flow depth

## Slide 19: Far-field top width
Elevation view looking downstream
Top width at reference and test flow depths (used in several, but not all ROTs)

## Slide 20: Bank full flow depth
Elevation view looking downstream
Bank full flow depth (used in several, but not all ROTs)

## Slide 21: Bank full flow width
Elevation view looking downstream
Bank full top width (used in several, but not all ROTs)

## Slide 22: Straight or Curved Channel
Categorical Variable

## Slide 23: Aligned or Skew Structure
Categorical Variable
No Skew (Skew Angle = 0)
Skew (Skew Angle > 10)

## Slide 24: Using the Tool -- Interface
Designer supplied input

## Slide 25: Using the Tool -- Interface
Intermediate Calculations

## Slide 26: Using the Tool -- Interface
ROT distances

## Slide 27: Using the Tool -- Interface
Method selection and reference
Selected distances

## Slide 28: Using the Tool – Illustrative Example
Consider the bridges pictured
  Determine where model boundaries should be placed to evaluate hydraulic impact of the pier(s)

## Slide 29: Using the Tool – Illustrative Example
Consider the bridges pictured
  Determine where model boundaries should be placed to evaluate hydraulic impact of the pier(s)

## Slide 30: Using the Tool – Illustrative Example
Consider upstream (pictured) bridge first

## Slide 31: Using the Tool – Illustrative Example
Consider upstream (pictured) bridge first
Flow

## Slide 32: Using the Tool – Illustrative Example
Bridge #1 Cross Section
Far-Field Cross Section

## Slide 33: Using the Tool – Illustrative Example Bridge #1
Reference Discharge : 1,180 cfs
Test Discharge : 50,615 cfs
Structure flow area: 8,400 sq. ft. (@ 30ft. deep)
Far field flow area: 14,100 sq. ft. (@ 30ft. deep)
Far field top width: 290 ft. (@ 30ft. deep)
Bank full flow depth: 10 ft.
Bank full flow width : 410 ft.
Curved or Straight Channel : Curved
Skewed or Aligned Hydraulic Structure : Aligned
Far-Field Cross Section

## Slide 34: Using the Tool – Illustrative Example

## Slide 35: Using the Tool – Illustrative Example
Bridge #2 Cross Section
Far-Field Cross Section

## Slide 36: Using the Tool – Illustrative Example Bridge #2
Reference Discharge : 1,180 cfs
Test Discharge : 50,615 cfs
Structure flow area: 7,500 sq. ft. (@ 30ft. deep)
Far field flow area: 14,100 sq. ft. (@ 30ft. deep)
Far field top width: 290 ft. (@ 30ft. deep)
Bank full flow depth: 10 ft.
Bank full flow width : 410 ft.
Curved or Straight Channel : Curved
Skewed or Aligned Hydraulic Structure : Aligned

## Slide 37: Using the Tool – Illustrative Example

## Slide 38: Using the Tool – Illustrative Example
Results: Using Method A if more than 2861 feet apart, can treat separately min-max distances on model representation
Other methods different distances (designer must choose the method they will adopt)
Flow
710
1416
724
1445
1445
724
710
1416
>2861

## Slide 39: Using the Tool – Illustrative Example
Results: Using Method A if less than 2861 feet apart, but more than 1431 feet apart, overlap on the upper ranges – designer must choose if treat as separate.
Other methods different distances (designer must choose the method they will adopt)
Flow
710
1416
724
1445
1445
724
710
1416
>1431

## Slide 40: Using the Tool – Illustrative Example
If model is to include BOTH bridges, then upstream condition at least 1416 feet upstream of bridge 1 and and 1445 feet downstream of bridge 2
Other methods different distances (designer must choose the method they will adopt)
Flow
710
1416
724
1445
1445
724
710
1416
>1431

## Slide 41: Summary
Tool to estimate model boundary locations based on a minimal description of the structure hydraulics and stream geometry
Helps avoid modeling an entire stream system for a change at one location, when a more localized model is appropriate (designer must decide)
Multiple methods are available:
  Methods A and C are relatively close in numerical output
  Methods B and D are relatively close in numerical output (but tend to be larger than A or C)